## Introduction
### RaspberryPi3-General Purpose Input Output (GPIO)
All Raspberry Pi models come with a 40 GPIO pins (P1 header) on the main board. It is used for digital I/O, communication protocols, PWM, and interrupts. The GPIO numbers are assigned by the Broadcom (BCM) chip. This design will describe to use of the digital I/O pins for controlling the connected LEDs and getting the state of the connected touch buttons.
The P1 header is connected to the front panel PCB of the Oradio3, on which the led indicators, touch buttons and volume button are located. These items are connected to the P1 header via the front panel PCB.

## The GPIO pin assignments for Oradio3
### The pin assignment for current version of the Oradio3.
The front panel PCB is connected to the P1 header using following pins.
Pin	Function	Pull-Up/Down	Usage
7	Output	Pull-Up	LED-PRESET3
15	Output	Pull-Up	LED-PLAY
23	Output	Pull-Up	LED-STOP
24	Output	Pull-Up	LED-PRESET1
25	Output	Pull-Up	LED-PRESET2
5	Input	Pull-Up	BUTTON-PRESET2
6	Input	Pull-Up	BUTTON-STOP
9	Input	Pull-Up	BUTTON-PLAY
10	Input	Pull-Up	BUTTON-PRESET3
11	Input	Pull-Up	BUTTON-PRESET

All the IO-pins require a Pull-Up configuration.
### The RaspiOS GPIO boot configuration
In the config file /boot/firmware/config.txt the low-level for the GPIO pins are set. The Raspberry Pi uses Device Tree (DT) overlays to configure the hardware, including GPIO pins. Overlays are applied using dtoverlay, e.g. to configure an I/O for i2c or UART. In our case we can define the outputs for the LEDs as follows in the config.txt:
gpio=23=op,dl	# output, driving low (LED-STOP)
gpio=24=op,dh	# output, driving high (LED-PRESET1)
gpio=25=op,dh	# output, driving high (LED-PRESET2)
gpio=7=op,dh	# output, driving high (LED-PRESET3)
gpio=15=op,dh	# output, driving high (LED-PLAY)
During boot time these settings will be applied to the output pins. The LED-STOP will be ON during boot-time
#### The python RPI.GPIO package
#### GPIO software interface
The package is available as pip package: https://pypi.org/project/Rpi.GPIO/. It provides a simple interface for configuring the pins as inputs or outputs, reading their state, and controlling them.
There are two ways of numbering the IO pins on a Raspberry Pi within Rpi.GPIO:
- The first is using the BOARD numbering system. This refers to the pin numbers on the P1 header of the Raspberry Pi board.
- The second numbering system is the BCM numbers. This is a lower level way of working - it refers to the channel numbers on the Broadcom SOC.
It is required to specify which numbering system is used.
A valuable function is GPIO.add_event_detect(). It is a function used in Raspberry Pi programming to set up an event detection on a specific GPIO pin. This allows the program to respond to changes in the pin's state, such as detecting when a button is pressed or released.
#### RPI.GPIO configuration programming
GPIO configuration	Instruction
Specify numbering system	GPIO.setmode(GPIO.BCM)
Input	GPIO.setup(channel, GPIO.IN)
Output	GPIO.setup(channel, GPIO.OUT)
Output with initial value	GPIO.setup(channel, GPIO.OUT, initial=GPIO.HIGH)
Pull up resistors	GPIO.setup(channel, GPIO.IN, pull_up_down=GPIO.PUD_UP)
Pull down resistors	GPIO.setup(channel, GPIO.IN, pull_up_down=GPIO.PUD_DOWN)
Events	GPIO.add_event_detect(channel, GPIO.RISING, callback=my_callback)
	Events can be GPIO.RISING, GPIO.FALLING or GPIO.BOTH.

#### Multi-user/Multi-task considerations for RPI.GPIO
The GPIO interface can be used by any user or task running on the Rpi3b. So it may require some protection to prevent unexpected results on I/O pins.
The RPI.GPIO library also offers good multi-task protections:
It offers atomicity on the GPIO writes: a call to GPIO.output(pin, state) the library makes a system call to write to either:
  - /sys/class/gpio/gpioX/value (sysfs interface), or
  - /dev/gpiomem (memory-mapped interface).
- This means the kernel guarantees that the write operation completes in one uninterruptible step.
- If two programs try to write to the same pin simultaneously, the kernel will serialize the writes. The second write will not interrupt the first—it will simply overwrite the result of the first write as soon as the first operation is done.
- The kernel does not stop or preempt a GPIO write operation to handle a new one. Instead, it processes writes in the order they are received (or as scheduled by the kernel’s process scheduler).
- The actual hardware register for the GPIO pin is updated immediately when the kernel processes the write. There is no "partial" or "interrupted" state for the pin.
#### GPIO Design decision
The GPIO library provides certain multi-task protections, but it has been decided to add a threading locking mechanism on a GPIO.output(). This is a Python built-in locking, and only works within a single python process. In case a system-wide lock is required, we need to use a locking which is file based.
## Top-down layered static view

The Oradio3 software layering typically consists of three main layers:
- the hardware abstraction layer (HAL), which includes the physical components.
- the middle-ware layer, which facilitates communication and data management between the hardware and applications. The OS services is considered to be part of this layer
- the application layer, where the actual software applications run and perform specific tasks.

The GPIOService class is a python module offering LED I/O service and BUTTON I/O service to other modules. It includes the Rpi.GPIO library to read from input pins or write to output pins.
The Rpi.GPIO library abstracts the details of the hardware interactions, providing a simplified API, and relies on RaspiOS for critical functionalities such as threading, memory management, and executing system commands. The RPi.GPIO library uses OS-level calls to toggle GPIO pins, taking advantage of the underlying operating system's capabilities.
The GPIO-controller is managing the I/O-registers of the broadcom chip.
## Detailed design of the gpio_service module.

### GPIOService Class
#### Purpose
- Provides a wrapper for button inputs and leds outputs, to hide the actual IO-pinning details
- Provides a callback for a button application to be notified if the state of a button changes
- The output to a pin is atomic, so is non-preemptive.
- Centralizes error handling and logging for I/O error
- The GPIO mode is set to GPIO.BCM
#### Design & Threading
- Singleton: Restricts the class to a single instance, to offer a single point of access for the gpio services.
- Thread Safety: Is provided by a python threading.locking on gpio.output(). The Rpi.GPIO library also provides guarantees on kernel level that the write operation completes in one uninterruptible step (atomicity).
- Events: The configured button event detection is a kernel-level edge-detection mechanism and uses a background watcher (internal notifier) inside the RPi.GPIO extension to dispatch callbacks.
Design Note:
To prevent certain race-conditions it is important to use the correct order during initialization of the GPIO events.
1. First the method set_button_edge_event_callback(self, callback) has to set the required callback for the caller.
2. Then the button events can be initialized with GPIOPIO.add_event_detect(channel, GPIO.RISING, callback=my_callback)
As soon as the event detection is initialized an edge detection event is found. In case no correct callback (e.g.None) is set, there will be an error, as the callback is not yet available.
#### API Reference
Constants/Defines:
LED_PLAY = "LedPlay"
LED_STOP = "LedStop"
LED_PRESET1 = "LedPreset1"
LED_PRESET2 = "LedPreset2"
LED_PRESET3 = "LedPreset3"
BUTTON_PLAY = "ButtonPlay"
BUTTON_STOP = "ButtonStop"
BUTTON_PRESET1 = "ButtonPreset1"
BUTTON_PRESET2 = "ButtonPreset2"
BUTTON_PRESET3 = "ButtonPreset3"

Method	Arguments	Returns
GPIOService.set_led_on	(led_name: str)	None
Description: / Thread-safe setting ON of a led / led_name is [LED_PLAY | LED_STOP | LED_PRESET1 | LED_PRESET2 | LED_PRESET3]

Method	Arguments	Returns
GPIOService.set_led_off	(led_name: str)	None
Description: / Thread-safe setting OFF of a led / led_name is [LED_PLAY | LED_STOP | LED_PRESET1 | LED_PRESET2 | LED_PRESET3]

Method	Arguments	Returns
GPIOService.get_led_state	(led_name: str)	True for led ON state, / False for led OFF state / None for unknown led name
Description: / Reads and returns the actual state of a led / led_name is [LED_PLAY | LED_STOP | LED_PRESET1 | LED_PRESET2 | LED_PRESET3]

Method	Arguments	Returns
GPIOService.get_button_state	(button_name: str)	True for a button press / False for a button not pressed / None for unknown button name
Description: / Reads and returns the actual state of a led / button_name is [BUTTON_PLAY | BUTTON_STOP | BUTTON_PRESET1 | BUTTON_PRESET2 | BUTTON_PRESET3]

Method	Arguments	Returns
GPIOService.enable_button_events	()	True for a button press / False for a button not pressed / None for unknown button name
Description:

Method	Arguments	Returns
GPIOService.set_button_edge_event_callback	(callback)	None
Description:

#### Error handling

Ccc

- All errors are logged using oradio_log.error or .warning.
- Exceeding block size logs an error immediately.
- Failed writes after all retries are logged as errors.
#### Attributes for module test
The class provides an attribute <gpio_module_test > to enable or disable module test functions within the class. This is used in the method _edge_callback() for performance measurements.

#### Module test
There is a module test program <gpio_service_test.py> that will provide following tests to test the methods of the class:
- All led-pins ON or OFF
- Single led-pin ON or OFF
- Polling the buttons state
- Button event-callback handling
- Unknown led or button error handling

### Chapters:
## Inhoudsopgave
Oradio I²C, Volume, and Backlighting Documentation	1
Overview	1
Key points:	2
Module: I2CService	2
Purpose	2
Design & Threading	2
API Reference	2
Error Handling	2
Stand-alone Test Program	2
Module: VolumeControl	2
Purpose	2
Design & Threading	3
ALSA Integration	3
API Reference	3
Stand-alone Test Program	3
Module: Backlighting	3
Purpose	3
Design & Threading	3
Sensor & DAC Handling	3
API Reference	3
Stand-alone Test Program	4
Architecture & Interconnections	4
Data Flow Examples:	4
Hardware & I²C Considerations	4
Dependencies	4
Notes & Best Practices	5
UML Class Diagram for Oradio I2C Modules	5

## Overview

### Explanation of the Layers
- Application Layer: This is where your Python scripts or applications reside. These scripts use RPi.GPIO to execute high-level operations to control the GPIO pins.
- RPi.GPIO as HAL: RPi.GPIO serves as the Hardware Abstraction Layer. It abstracts the details of the hardware interactions, providing a simplified API that allows developers to interact with GPIO without managing low-level tasks. For example, when you use RPi.GPIO.output(pin, state) to set a GPIO pin high or low, RPi.GPIO handles the specific commands needed to manipulate the pin.
- Operating System Layer: RPi.GPIO relies on RaspiOS (an operating system based on Debian) for critical functionalities such as threading, memory management, and executing system commands. The RPi.GPIO library uses OS-level calls to toggle GPIO pins, taking advantage of the underlying operating system's capabilities.
- Hardware Layer: Ultimately, the GPIO pins on the Raspberry Pi are the physical components that RPi.GPIO controls. The hardware layer is where the actual electrical signals are manipulated to connect with external devices.

In this architecture, RPi.GPIO plays a dual role. It serves as a Hardware Abstraction Layer while also relying on the capabilities of the operating system layer to function effectively. This layered approach allows for seamless communication between the application and the hardware, promoting cleaner code and easier maintenance.

### 1. How Locking Works Between Independent Programs
- Since the programs are independent, you can’t use Python’s built-in threading.Lock (which only works within a single process).
- Instead, you need a system-wide lock, such as:
  - A lock file (a file whose existence indicates the lock is held).
  - A named system semaphore (using posix_ipc or similar).
  - A database or Redis lock (if you have those services running).

### 2. Simple Lock File Approach
Here’s a practical example using a lock file in /tmp/. Both programs can use this to coordinate access to a GPIO pin.
#### Shared Lock File Logic
python
Copy
import os
import time
import fcntl # For file locking (optional, but recommended)

LOCK_FILE = "/tmp/gpio_pin17.lock"

def acquire_lock():
    # Open the lock file in write mode (creates it if it doesn't exist)
    lock_fd = open(LOCK_FILE, "w")
    try:
        # Try to acquire an exclusive lock (non-blocking)
        fcntl.flock(lock_fd, fcntl.LOCK_EX | fcntl.LOCK_NB)
        return lock_fd # Return the file descriptor if lock is acquired
    except IOError:
        # Lock is held by another process
        return None

def release_lock(lock_fd):
    # Release the lock and close the file
    fcntl.flock(lock_fd, fcntl.LOCK_UN)
    lock_fd.close()
    os.remove(LOCK_FILE)

# Example usage:
lock_fd = acquire_lock()
if lock_fd:
    try:
        # Safe to access GPIO pin 17 here
        print("Acquired lock, accessing GPIO pin 17...")
        time.sleep(2) # Simulate work
    finally:
        release_lock(lock_fd)
else:
    print("Could not acquire lock, GPIO pin 17 is busy.")