## Introduction
The oradio_control is based on a state machine.

### Introduction into UML state diagrams
A state diagram models the behavior of a system or an object in response to events. A state diagram mainly consists of states, events, guards, transitions, and actions. It’s a behavioral diagram and it represents the behavior using finite state transitions.
#### Initial state
It shows the starting point of the system. It’s represented as a filled circle

#### Final State
It shows the ending point of the system. It’s represented as a circle with a dot inside

#### Entry Point
An input connector for control flow into an activity from outside (named) — used when connecting activities across activity partitions or when reusing activity nodes.

#### Exit Point
An output connector for control flow leaving an activity to outside; used to indicate exit from an activity (named).

#### Events
An event can be a signal,trigger or a change in the environment of the system. Events may or may not lead to a change in the system’s state
#### States
A state represents the conditions or circumstances of an object of a class at an instant of time.
- StateName: The name of the state
- event: trigger that causes the transition.
- /action: An operation executed in response to an accepted event
State actions are invoked when the system is in a specific state. There are 3 types of state actions:
- Entry actions: they are executed when the system enters the state
- Do actions: they are continuously executed while the system is in the state
- Exit actions: they are executed when the system exits the state

#### Transitions
Transitions are shown as arrows from one state to another. They may have three indicators written on them:
- The event that triggers the transition
- The guard statement which is a condition that must be true for the transition to take place
- An action statement that will happen as a result of the transition

[isSpotifyConnected]
ButtonPlay
/playSound()
/setLed()
/startSpotifyPlayback()

#### Composite State
A state that has substructure and internal behavior. It can contain one or more regions, which can contain one or more states. The state diagrams are executed in parallel.

#### Concurrent regions
Represent separate areas of concern within a state, allowing for independent state transitions in each region, simultaneously.

#### Package
The UML design symbol for a package is depicted as a tabbed folder, which represents a container for grouping related UML elements.

### Introduction into State transition diagrams
a state-transition table is a table showing what state a finit-state machine will move to, based on the current state and other inputs. It is essentially a truth table in which the inputs include the current state along with other inputs, and the outputs include the next state along with other outputs.
Current State	Event	Condition(guards)	Next State	Action

## The Oradio state diagrams views
### The OradioMain state diagram

### The OradioMain composite state
#### State diagram

#### State table
Current State	Event	Condition	Next State	Action
OradioCreation	criticalError	None	ErrorHandling	goto_error()
	creationDone	None	MpdCreation	start_mpd_creation()
MpdCreation	usbAbsent	None	ErrorHandling	goto_error()
	usbPresent	None	ErrorHandling	goto_error()
	timeOut	None	ErrorHandling	goto_error()
	mpdCreationDone	None	Standby
	criticalError	None	ErrorHandling	goto_error()
Standby	ButtonPreset1, / ButtonPreset2, / ButtonPreset3	None	MpdPlaying	playSound() / setLed() / startMpdPlayback()
	VolumeChanged	None	MpdPlaying	startMpdPlayback()
	ButtonPlay	not isSpotifyConnected	MpdPlaying	playSound() / setLed) / startMpdPlayback()
	VolumeChanged	None	MpdPlaying	startMpdPlayback()
	CriticalError	None	ErrorHandling	goto_error()
	ButtonPlay	isSpotifyConnected	SpotifyPlaying	playSound() / setLed() / startSpotifyPlayback()
MpdPlaying	ButtonStop	None	Standby	gotoStandby()
	CriticalError	None	ErrorHandling	goto_error()
SpotifyPlaying	ButtonStop	None	Standby	gotoStandby()
	CriticalError	None	ErrorHandling	goto_error()

### Other state handler as packages

## Top-down layered static view

TBD

## Detailed design of the oradio_control module.

### Classess
#### Purpose
#### Design & Threading
#### API Reference
##### BUTTONS Constants

##### Methods:

#### Error handling

#### Attributes for module test

### Module test