# Librespot & mDNS Service Discovery on Linux
## Overview
This document outlines how librespot interacts with the mDNS stack on Linux systems, specifically through avahi-daemon, nss-mdns, and optionally systemd-resolved. It also provides guidance for configuring these components to avoid hostname conflicts and ensure smooth multi-device operation.
## Protocols
1. Multicast DNS (mDNS) is a computer networking protocol that resolves hostnames to IP addresses within small networks that do not include a local name server. It is a zero-configuration service, using essentially the same programming interfaces, packet formats and operating semantics as unicast Domain Name System (DNS). It was designed to work as either a stand-alone protocol or compatible with standard DNS servers. It uses IP multicast User Datagram Protocal (UDP) packets and is implemented by the Apple Bonjour and open-source Avahi software packages, included in most Linux distributions.
2. DNS Service Discovery (DNS-SD) is a way of using standard DNS programming interfaces, servers, and packet formats to browse the network for services. It can also be be used for mDNS to yield zero-configuration DNS-SD. This uses DNS PTR, SRV or TXT records to advertise instances of service types, domain names for those instances, and optional configuration parameters for connecting to those instances. But SRV records can now resolve to .local domain names, which mDNS can resolve to local IP addresses.
## Hostname
In computer networking, a hostname is a label that is assigned to a device connected to a compute network and that is used to identify the device on the network, such as the World Wide Web. Hostnames may be simple names consisting of a single word or phrase, or they may be structured. Each hostname usually has at least a network address associated with it for routing packets for performance and other reasons.
Internet hostnames may have appended the name of a DNS domain, separated from the host-specific label by a period ("dot"). In the latter form, a hostname is also called a domain name. If the domain name is completely specified, including a TLD (top-level-domain: the domain at the highest level in hierarchical DSN of the Internet), then the hostname is said to be a fully qualified domain name (FQDN). Hostnames that include DNS domains are often stored in the Domain Name System together with the IP address of the host they represent for the purpose of mapping the hostname to an address, or the reverse process.
## Components Involved
Librespot
  1. Is an open source client library for Spotify. It enables applications to use Spotify's service to control and play music via various backends, and to act as a Spotify Connect receiver.
  2. Advertises itself via mDNS to appear as a Spotify target device.
  3. See git-hub/librespot
1. avahi-daemon
  1. Implements mDNS and DNS-SD on Linux.
  2. Publishes host and service records to the local network.
  3. Handles hostname conflict resolution (e.g., oradio becoming oradio-2).
2. Nss-mdns (Name Service Switch)
  1. The Name Service Switch (NSS) is a feature found in the standard C library of various Unix-like operating systems that connects a computer with a variety of sources of common configuration databases and name resolution mechanisms.
  2. These sources include local operating system files (such as /etc/passwd, /etc/group, and /etc/hosts), the Domain Name System (DNS), the Network Information Service (NIS, NIS+), and LDAP.
  1. Allows the system's glibc name resolution (via /etc/nsswitch.conf) to resolve .local mDNS hostnames using Avahi.
  1. Required for ping oradio.local to work without DNS.
2. system-resolved
  1. Manages name resolution, DNS over TLS, and local caching.
  2. Can conflict with nss-mdns if both attempt mDNS handling.

Component	Purpose	Should it be enabled
systemd-resolved	DNS resolver, integrates with resolvectl	Yes
nss-mdns	Handles .local mDNS via Avahi	Yes
avahi-daemon	Advertises/discovers .local services	Yes
/etc/nsswitch.conf	Configures which resolver to use	Yes, when properly set

## Interaction between these services
The nsswitch (via nss-mdns) and avahi-daemon use the D-Bus, but they do so in different ways:
nsswitch and nss-mdns:
  - The Name Service Switch (nsswitch.conf) itself does not use D-Bus directly.
  - The nss-mdns module, which enables mDNS name resolution via NSS, communicates directly with Avahi (or another mDNS provider like systemd-resolved).
  - nss-mdns does not need D-Bus—it simply intercepts hostname lookups and queries Avahi or the network.
Avahi-daemon:
  - avahi-daemon does use D-Bus for:
    - Providing service discovery data to applications.
    - Allowing applications to register services dynamically.
    - Broadcasting events when services appear or disappear.
  - Applications (like a media player) can use D-Bus to talk to Avahi and discover _http._tcp or _spotify-connect._tcp services.
How they interact:
  - nss-mdns (via nsswitch.conf) queries Avahi when resolving .local hostnames.
  - avahi-daemon listens for these queries and responds with the appropriate IP.
  - Avahi can also broadcast service discovery info using D-Bus, which is used by applications needing to discover services dynamically.
## Hostname Conflict Resolution
When multiple devices on the same LAN share the same hostname conflicts may arise w.r.t. DNS lookup. This conflict needs to be resolved. The avahi-daemon can handle hostname conflicts:
- It listens to incoming mDNS queries and responses from other devices
- It periodically announces registered services (like _spotify-connect._tcp) to the local network using mDNS.
- The avahi-deamon service runs in background and sends out probe packets to check if the name is already in use on the network. In case of a conflict it will automatically resolve the hostname, appending a number (e.g., oradio-2).
- This new hostname is resolved and published.
To test the mDNS resolution following commands can be used:
1. get your (WLAN) IP address: e.g. with ifconfig
2. get the (new) hostname: avahi-resolve -a <your_ip_address> | awk '{print $2 }')

## Name Service Switch(nss) conflict resolution
It is important that NSS uses the correct hosts priority path to resolve the hostname. There are several resolve sources available. These are defined in the hosts parameter of /etc/nsswitch.conf.
For Oradio the best lookup order will be.
Hosts: files mdns4_minimal [NOT_FOUND=return] dns
What does it do::
- files: First check /etc/hosts
- mdns4_minimal: Then check mDNS
- dns: then fall back to DNS (provided by your local router)
This ensures .local names are handled via mDNS before checking DNS.
## Librespot Conflict Resolution
The tricky thing with Librespot is that it provides a name in its confuguration which will used be during spotify discovery. Either via an environment variable or via an argument in the librespot call.
- Environment="LIBRESPOT_NAME=Oradio"
- ExecStart=/usr/bin/librespot --name Oradio
As this will be used in every Oradio running on the same network. Each mDNS advertisement will get the same name “Oradio”. This will cause a conflict at Spotify, as it can only handle one. What will happen is unpredictable. Sometimes only one Oradio is listed in Spotify, sometimes there is no Oradio listed.
So we have to enforce a different (unique) name for the mDNS name librespot is using. Good news is that avahi-daemon already has resolved the conflict by adding a subnumber to the hostname (e.g. oradio-2).
With avahi-resolve command we can get info on the new hostname. However we have to wait until avahi-daemon has resolved the naming conflict. As the naming conflict will arise at boot-time we have the set the dependency between these service correctly.
### Boot-Time Activity Diagram
[ boot ]
   |
   |---> systemd starts
        |
        |---> dbus
        | |
        | '---> avahi-daemon
        | |
        | '---> Publishes hostname (conflict resolution if needed)
        |
        |---> systemd-resolved
        | '---> May handle DNS and mDNS (conflicts with nss-mdns if not disabled)
        |
        '---> librespot service starts
        |
        '---> Uses Avahi to publish _spotify-connect._tcp service

This is the desired order (and dependancy) as librespot needs the (new) hostname resolved by avahi-daemon. As there is no direct interaction between librespot and avahi-daemon we need aan additional service that reads the new hostname and provides it to librespot as new name to use.
The following service can do this.

publishing_oradio_librespot.service:
=====================================
[Unit]
Description=Enable local hostname via Avahi
After=network-online.target avahi-daemon.service
Wants=avahi-daemon.service
[Service]
Type=oneshot
ExecStart=/home/pi/Oradio3/shell_scripts/publishing_oradio_librespot.sh
RemainAfterExit=true
[Install]
WantedBy=multi-user.target

This will call a shell-script called publishing_oradio_librespot.sh

#!/bin/bash
# Get the current IP address
IP_ADDRESS=$(ifconfig wlan0 | grep 'inet ' | awk '{print $2}')
# Get the current hostname
AVAHI_HOSTNAME=$(avahi-resolve -a $IP_ADDRESS |awk '{print $2}' | cut -d'.' -f1)
LIBRESPOT_NAME=$AVAHI_HOSTNAME "
# assign AVAHI_HOSTNAME to LIBRESPOT_NAME in librespot.service
sudo sed -i "s/LIBRESPOT_NAME=.*/LIBRESPOT_NAME=$AVAHI_HOSTNAME\"/g" /etc/systemd/system/librespot.service

By using this script the librespot.service file is modified w.r.t. the LIBRESPOT_NAME to use during advertisement.
It is important that this modified librespot.service file is ready before the librespot service is executed. So the boot timing will be:
[ boot ]
   |
   |---> systemd starts
        |
        |---> dbus
        | |
        | '---> avahi-daemon
        | |
        | '---> Publishes hostname (conflict resolution if needed)
        |
        |---> systemd-resolved
        | '---> May handle DNS and mDNS (conflicts with nss-mdns if not disabled)
        |
        |-→ publishing_oradio_librespot (queries avahi via avahi-resolve for final hostname
        |
        '---> librespot service starts
        |
        '---> Uses Avahi to publish _spotify-connect._tcp service
## Configuration
### Nsswitch.conf:
It is important that the nsswitch.conf is configured correctly to prioritize the mDNS
Look for line “hosts:” in /etc/nsswitch.conf and change it to:
hosts: files mdns4_minimal [NOTFOUND=return] dns
who does it do::
- First check /etc/hosts
- Then check mDNS (mdns4_minimal)
- Then fall back to DNS (provided by your local router)
This ensures .local names are handled via mDNS before checking DNS.
### Avahi-daemon.conf
### /etc/avahi/avahi-daemon.conf settings

[server]
domain-name=local
use-ipv4=yes
use-ipv6=no
allow-interfaces=wlan0

[wide-area]
enable-wide-area=no

[publish]
publish-address=yes
publish-domain=yes

domain-name= Set the default domain name avahi-daemon tries to register its host name and services on the LAN in. If omitted defaults to ".local".
use-ipv4= Takes a boolean value ("yes" or "no"). If set to "no" avahi-daemon will not use IPv4 sockets. Default is "yes".
use-ipv6= Takes a boolean value ("yes" or "no"). If set to "no" avahi-daemon will not use IPv6 sockets. Default is "yes".
allow-interfaces= Set a comma seperated list of allowed network interfaces that should be used by the avahi-daemon. Other interfaces will be ignored. If set to the empty list all local interfaces except loopback and point-to-point will be used.
enable-wide-area= Takes a boolean value ("yes" or "no"). Enable wide-area DNS-SD, aka DNS-SD over unicast DNS. If this is enabled only domains ending in .local will be resolved on mDNS, all other domains are resolved via unicast DNS. If you want to maintain multiple different multicast DNS domains even with this option enabled we encourage you to use subdomains of .local, such as "kitchen.local". This option defaults to "yes". This is set to “no” to prevent a local router to provide also a mDNS resolution, which may interfere with the local mDNS resolve.
publish-addresses= Takes a boolean value ("yes" or "no"). If set to "yes" avahi-daemon will register mDNS address records for all local IP addresses. Unless you want to use avahi-daemon exclusively for browsing it's recommended to enable this. If you plan to register local services you need to enable this option. Defaults to "yes".
publish-domain= Takes a boolean value ("yes" or "no"). If set to "yes" avahi-daemon will announce the locally used domain name (see above) for browsing by other hosts. Defaults to "yes".

### Avahi services for librespot naming resolution
See avahi-wiki for more info.
Avahi advertises the services whose *.service files are found in /etc/avahi/services. Files in this directory must be readable by the avahi user/group.
If you want to advertise a service for which there is no *.service file, we have to create such service file. As we need to advertise for _spotify-connect._tcp we have to create a service file doing this.

<?xml version="1.0" standalone='no'?>
<!DOCTYPE service-group SYSTEM "avahi-service.dtd">

<service-group>
  <name replace-wildcards="yes">SpotifyConnect %h</name>
  <service>
    <type>_spotify-connect._tcp</type>
    <port>45305</port>
    <txt-record>VERSION=1.0</txt-record>
    <txt-record>DESCRIPTION=SpotifyConnect Service</txt-record>
    <txt-record>CPath=/zeroconf</txt-record>
  </service>

</service-group>

<service-group> The document tag of avahi service files. Should contain one <name> and one or more <service> elements.
<name replace-wildcards="yes|no"> The service name. If replace-wildcards is "yes", any occurrence of the string "%h" will be replaced by the local host name. Here we use “SpotifyConnec” as service names . If replace-wildcards is not specified, defaults to "no".
<type> Contains the DNS-SD service type for this service. e.g. "_http._tcp".
<port> The IP port number the service listens on.
<txt-record value-format="text|binary-hex|binary-base64"> DNS-SD TXT record data. If value-format is "text", the value of the TXT record is taken verbatim