## Introduction
### RaspberryPi3-General Purpose Input Output (GPIO)
All Raspberry Pi models come with a 40 GPIO pins on the main board. It is used for digital I/O, communication protocols, PWM, and interrupts. The GPIO numbers are assigned by the Broadcom (BCM) chip. This design will describe to use of the digital I/O pins for controlling the connected LEDs and getting the state of the connected touch buttons.
#### The GPIO pin numbering/assignments:

Figure 1: The 40 pins P1 header
The pin assignment for current version of the Oradio3.
Pin	Function	Pull-Up/Down	Usage
7	Output	Pull-Up	LED-PRESET3
15	Output	Pull-Up	LED-PLAY
23	Output	Pull-Up	LED-STOP
24	Output	Pull-Up	LED-PRESET1
25	Output	Pull-Up	LED-PRESET2
5	Input	Pull-Up	BUTTON-PRESET2
6	Input	Pull-Up	BUTTON-STOP
9	Input	Pull-Up	BUTTON-PLAY
10	Input	Pull-Up	BUTTON-PRESET3
11	Input	Pull-Up	BUTTON-PRESET

#### The RaspiOS GPIO boot configuration
In the config file /boot/firmware/config.txt the low-level for the GPIO pins are set. The Raspberry Pi uses Device Tree (DT) overlays to configure the hardware, including GPIO pins. Overlays are applied using dtoverlay, e.g. to configure an I/O for i2c or UART. In our case we can define the outputs for the LEDs as follows in the config.txt:
gpio=23=op,dl	# output, driving low (LED-STOP)
gpio=24=op,dh	# output, driving high (LED-PRESET1)
gpio=25=op,dh	# output, driving high (LED-PRESET2)
gpio=7=op,dh	# output, driving high (LED-PRESET3)
gpio=15=op,dh	# output, driving high (LED-PLAY)
During boot time these settings will be applied to the output pins.
#### The python RPI.GPIO package
The package is available as pip package: https://pypi.org/project/Rpi.GPIO/. It provides a simple interface for configuring the pins as inputs or outputs, reading their state, and controlling them.
There are two ways of numbering the IO pins on a Raspberry Pi within Rpi.GPIO:
- The first is using the BOARD numbering system. This refers to the pin numbers on the P1 header of the Raspberry Pi board.
- The second numbering system is the BCM numbers. This is a lower level way of working - it refers to the channel numbers on the Broadcom SOC.
It is required to specify which numbering system is used.
A valuable function is GPIO.add_event_detect(). It is a function used in Raspberry Pi programming to set up an event detection on a specific GPIO pin. This allows the program to respond to changes in the pin's state, such as detecting when a button is pressed or released.
#### RPI.GPIO configuration programming
GPIO configuration	Instruction
Specify numbering system	GPIO.setmode(GPIO.BCM)
Input	GPIO.setup(channel, GPIO.IN)
Output	GPIO.setup(channel, GPIO.OUT)
Output with initial value	GPIO.setup(channel, GPIO.OUT, initial=GPIO.HIGH)
Pull up resistors	GPIO.setup(channel, GPIO.IN, pull_up_down=GPIO.PUD_UP)
Pull down resistors	GPIO.setup(channel, GPIO.IN, pull_up_down=GPIO.PUD_DOWN)
Events	GPIO.add_event_detect(channel, GPIO.RISING, callback=my_callback)
	Events can be GPIO.RISING, GPIO.FALLING or GPIO.BOTH.

## Detailed design of GPIOService class

# Module: I2CService
## Purpose
- Encapsulates all I²C communication.
- Provides a thread-safe API for reading/writing bytes and blocks.
- Centralizes error handling and logging for I²C operations.
- Supports retries and backoff for write operations.
## Design & Threading
- Singleton: Only one instance exists to prevent multiple threads from accessing SMBus simultaneously.
- Thread Safety: All SMBus operations are guarded by a threading.Lock.
- Retry Logic: Write operations retry I2C_RETRIES times with I2C_BACKOFF seconds delay.
## API Reference
Method	Description
read_byte(device, register)	Thread-safe read of a single byte. Returns int or None on failure.
write_byte(device, register, value)	Thread-safe write of a single byte with retry/backoff.
read_block(device, register, length)	Reads up to 32 bytes. Returns list[int] or None.
write_block(device, register, data)	Writes up to 32 bytes with retry/backoff.

## Error Handling
- All errors are logged using oradio_log.error or .warning.
- Exceeding block size logs an error immediately.
- Failed writes after all retries are logged as errors.
## Stand-alone Test Program
- Scans /dev/i2c-* to find available buses.
- Probes expected devices (MCP3021, TSL2591, MCP4725, HUSB238).
- Reports missing and unexpected devices using color-coded console output.

## Top-Down static view
The software layering standard typically consists of three main layers:
- the hardware layer (HAL), which includes the physical components.
- the middle-ware layer, which facilitates communication and data management between the hardware and applications. The OS services is considered to be part of this layer
- the application layer, where the actual software applications run and perform specific tasks.

### Chapters:
## Inhoudsopgave
Oradio I²C, Volume, and Backlighting Documentation	1
Overview	1
Key points:	2
Module: I2CService	2
Purpose	2
Design & Threading	2
API Reference	2
Error Handling	2
Stand-alone Test Program	2
Module: VolumeControl	2
Purpose	2
Design & Threading	3
ALSA Integration	3
API Reference	3
Stand-alone Test Program	3
Module: Backlighting	3
Purpose	3
Design & Threading	3
Sensor & DAC Handling	3
API Reference	3
Stand-alone Test Program	4
Architecture & Interconnections	4
Data Flow Examples:	4
Hardware & I²C Considerations	4
Dependencies	4
Notes & Best Practices	5
UML Class Diagram for Oradio I2C Modules	5

## Overview

### Explanation of the Layers
- Application Layer: This is where your Python scripts or applications reside. These scripts use RPi.GPIO to execute high-level operations to control the GPIO pins.
- RPi.GPIO as HAL: RPi.GPIO serves as the Hardware Abstraction Layer. It abstracts the details of the hardware interactions, providing a simplified API that allows developers to interact with GPIO without managing low-level tasks. For example, when you use RPi.GPIO.output(pin, state) to set a GPIO pin high or low, RPi.GPIO handles the specific commands needed to manipulate the pin.
- Operating System Layer: RPi.GPIO relies on RaspiOS (an operating system based on Debian) for critical functionalities such as threading, memory management, and executing system commands. The RPi.GPIO library uses OS-level calls to toggle GPIO pins, taking advantage of the underlying operating system's capabilities.
- Hardware Layer: Ultimately, the GPIO pins on the Raspberry Pi are the physical components that RPi.GPIO controls. The hardware layer is where the actual electrical signals are manipulated to connect with external devices.

In this architecture, RPi.GPIO plays a dual role. It serves as a Hardware Abstraction Layer while also relying on the capabilities of the operating system layer to function effectively. This layered approach allows for seamless communication between the application and the hardware, promoting cleaner code and easier maintenance.

### 1. How Locking Works Between Independent Programs
- Since the programs are independent, you can’t use Python’s built-in threading.Lock (which only works within a single process).
- Instead, you need a system-wide lock, such as:
  - A lock file (a file whose existence indicates the lock is held).
  - A named system semaphore (using posix_ipc or similar).
  - A database or Redis lock (if you have those services running).

### 2. Simple Lock File Approach
Here’s a practical example using a lock file in /tmp/. Both programs can use this to coordinate access to a GPIO pin.
#### Shared Lock File Logic
python
Copy
import os
import time
import fcntl # For file locking (optional, but recommended)

LOCK_FILE = "/tmp/gpio_pin17.lock"

def acquire_lock():
    # Open the lock file in write mode (creates it if it doesn't exist)
    lock_fd = open(LOCK_FILE, "w")
    try:
        # Try to acquire an exclusive lock (non-blocking)
        fcntl.flock(lock_fd, fcntl.LOCK_EX | fcntl.LOCK_NB)
        return lock_fd # Return the file descriptor if lock is acquired
    except IOError:
        # Lock is held by another process
        return None

def release_lock(lock_fd):
    # Release the lock and close the file
    fcntl.flock(lock_fd, fcntl.LOCK_UN)
    lock_fd.close()
    os.remove(LOCK_FILE)

# Example usage:
lock_fd = acquire_lock()
if lock_fd:
    try:
        # Safe to access GPIO pin 17 here
        print("Acquired lock, accessing GPIO pin 17...")
        time.sleep(2) # Simulate work
    finally:
        release_lock(lock_fd)
else:
    print("Could not acquire lock, GPIO pin 17 is busy.")

### 3. How It Works
- acquire_lock(): Tries to create and lock a file. If the file is already locked by another process, it fails (non-blocking).
- release_lock(): Releases the lock and deletes the file.
- Both programs use the same LOCK_FILE path, so they compete for the same lock.

### 4. Why This Works
- The lock is system-wide because it’s based on a file in /tmp/, which all programs can access.
- The fcntl.flock call ensures atomic locking at the OS level, so there’s no race condition.
- If one program crashes, the lock file remains, but you can add a timeout or cleanup logic to handle this.

### 5. Alternative: Named Semaphore
If you prefer, you can use a named semaphore (requires posix_ipc):
python
Copy
from posix_ipc import Semaphore

SEM_NAME = "/gpio_pin17_semaphore"

def acquire_semaphore():
    try:
        sem = Semaphore(SEM_NAME, flags=0o600, initial_value=1)
        sem.acquire()
        return sem
    except:
        return None

def release_semaphore(sem):
    sem.release()
    sem.unlink() # Only unlink if you're done with it permanently

### 6. Important Notes
- Lock files/semaphores are advisory: Both programs must agree to use the lock. If one ignores it, conflicts can still occur.
- Cleanup: Always release the lock in a finally block to avoid deadlocks.
- Timeouts: Consider adding a timeout to avoid indefinite waiting.

### Summary Table
Approach	Pros	Cons
Lock File	Simple, no extra dependencies	Needs cleanup, advisory only
Named Semaphore	More robust, OS-managed	Requires posix_ipc

### . Atomicity of GPIO Writes
- When you call GPIO.output(pin, state) in Rpi.GPIO, the library makes a system call to write to either:
  - /sys/class/gpio/gpioX/value (sysfs interface), or
  - /dev/gpiomem (memory-mapped interface).
- These writes are atomic at the kernel level. This means the kernel guarantees that the write operation completes in one uninterruptible step.
- If two programs try to write to the same pin simultaneously, the kernel will serialize the writes. The second write will not interrupt the first—it will simply overwrite the result of the first write as soon as the first operation is done.

### 2. No Preemption or Interruption
- The kernel does not stop or preempt a GPIO write operation to handle a new one. Instead, it processes writes in the order they are received (or as scheduled by the kernel’s process scheduler).
- The actual hardware register for the GPIO pin is updated immediately when the kernel processes the write. There is no "partial" or "interrupted" state for the pin.

### 3. Practical Implications
- If Program A sets pin1 to HIGH and, a microsecond later, Program B sets pin1 to LOW, the pin will end up as LOW. Program A’s write is not interrupted—it is simply overwritten by Program B’s write.
- There is no error or warning unless there’s a permission issue or the pin is not exported.